## Slide 1: آشنایی با زبانهای توصیف سخت افزار و FPGA
احسان یزدیان
بهمن ماه 1403
باسمه تعالی

## Slide 2: Introduction
What is an FPGA?
Field Programmable Gate Array

## Slide 3: What is Inside an FPGA?
FPGA Basic Structure
Configurable
Logic
Blocks
I/O
Blocks

## Slide 4: One of My Projects Implemented on FPGA
FPGA, ASIC or DSP?

## Slide 5: How to Implement a Design
ASIC
Application Specific
Integrated Circuit
User
Programmable
PLD
Programmable Logic
Devices
FPGA
DSP
Software
Programmable
Flexibility
Performance
ASIC
FPGA
DSP

## Slide 6: Technology Timeline

## Slide 7: Advantages of FPGA
Offer the advantages of high integration
  High complexity, density, reliability
  Low cost, power consumption, small physical size
Avoid the problems of ASICs
  high NRE (Non-recurring engineering)
  long delay in design and testing

## Slide 8: Advantages of FPGA
  Time To Market
  Design Cycle

## Slide 9: Advantages of FPGA
Faster than microcontrollers and microprocessors and GPUs.
  Parallel Processing
FPGA technology allows you to embed a processor, ROM, RAM, DSP, and any other block onto a single chip
  This is replacing a lot of ICs.

## Slide 10: IC Designs Decrease
Ideal for customized designs
  Product differentiation in a fast-changing market
  IC Designs Decrease

## Slide 11: Introduction
FPGA design and programming Skills:
FPGA Architecture
Synthesis & Implementation Tools
HDL Programming

## Slide 12: Introduction to PLDs
Integrated Circuits
ASIC
User
Programmable
PLD
FPGA
PAL
PLA
CPLD
PROM

## Slide 13: Programmable Logic Devices: PLDs
Logic Function
Different Types
SUM of PRODUCTS
Prefabricated
Programmble Links
Reconfigurable

## Slide 14: PLDs

## Slide 15: Complex PLDs
Array of PAL-like devices, interconnected by a switch matrix
Programmable PLD Blocks and interconnections.
Electrically Erasable links
Central Switch Matrix
PAL Block
PAL Block
Dedicated
inputs
Clock/
Inputs
PAL Block
PAL Block
I/Os
I/Os
I/Os
I/Os

## Slide 16: Proposed FPGA Boards
Mojo PLUS (محصول ایرانی)
  Spartan 6 XC6SLX9 FPGA + ARM Cortex M3
  84 digital IO pins, 8 analog inputs (10 and 12 bits width)
  32 Mbit Flash memory
  8 general purpose LEDs
  USB Programable
  Price: 360 هزارتومان

## Slide 17: Proposed FPGA Boards
تراشه‌ی Xilinx Spartan6-LX9
۴ مگابیت حافظه‌ی SRAM
واسط USB 2.0 با سرعت ۱۰MB/s
پروگرامر USB روی بورد؛ قابلیت پیکره‌بندی FPGA و SPI Flash از طریق پروگرامر usb-jtag تعبیه‌شده روی بورد
توسعه‌ی وسائل جانبی (از طریق کانکتور بال Wing)
قیمت: 1 میلیون تومان
شرکت ترنج رایانه نصف جهان

## Slide 18: Proposed FPGA Boards
Z-turn Board
  667MHz Xilinx XC7Z010/020 Dual-core ARM Cortex-A9 Processor with Xilinx 7-series FPGA logic - 1GB DDR3 SDRAM (2 x 512MB, 32-bit), 16MB QSPI Flash - USB_UART, USB2.0 OTG, 10/100/1000Mbps Ethernet, HDMI, TF, … - Onboard Three-axis Acceleration Sensor and Temperature Sensor

## Slide 19: مقدمه
مباحث درس:
  آشنایی با FPGA و زبانهای توصیف سخت افزار
  زبان برنامه نویسی سخت افزار Verilog HDL
  ساختار داخلی FPGA و بلوک های آماده سخت افزاری
  آشنایی با نرم افزارهای شبیه سازی
  فرآیندهای سنتز، پیاده سازی و برنامه ریزی FPGA
  آشنایی با تکنیکهای برنامه نویسی و طراحی
  بهینه سازی طراحی سخت افزار (آشنایی با معیارها و روشهای بهینه سازی)
  استفاده از هسته های نرم در طراحی مدارات
  طراحی ماژولهای پردازش سیگنال در محیط Matlab
  آشنایی با محیط Vivado و برنامه نویسی HLS و آشنایی با تراشه های Zynq
  استفاده از هسته نرم MicroBlaze و فراگیری Embedded Design
ارزشیابی:
  کوئیز و حضور 4 نمره
  تکلیف و پروژه 5 نمره
  میان ترم + پایان ترم 11 نمره

## Slide 20: مراجع درس و نرم افزارها
  مراجع:
Samir Palnitkar, Verilog HDL: A Guide to Digital Design and Synthesis, 2nd Edition, 2003.
P. Chu, FPGA Prototyping by Verilog Examples, Wiley, 2008.
James M. Lee, VERILOG® QUICKSTART, 3rd Edition, 2002.
Steve Kilts, Advanced FPGA Design, John Wiley, 2007.
حسین کریمیان، فریبا حیدری، طراحی و مدلسازی مدارهای دیجیتال با Verilog HDL، 1382.
  Many Online resources
نرم افزارها: (موجود بر روی سامانه software.iut.ac.ir)
Xilinx ISE Design Software
ModelSim
Xilinx Vivado Design Suite
Matlab & SysGen