## Slide 1: FPGA basic Structure and Concept of synthesis
احسان یزدیان
بهمن 1403
باسمه تعالی

## Slide 2: Concept of Synthesis
  FPGA has Large Number of Logic Block ‘Islands’ in a ‘Sea’ of Interconnects
Example: Designing a Full Adder
We can implement this design in FPGA using FPGA programming softwares.
We can put these blocks together to design multi-bit adders.
Real projects are much more complex than this simple adder.
Full Adder

## Slide 3: Hardware Design Languages (Verilog)
Behavioural codes instead of gate level design.
  Verilog, VHDL, ....
Example of verilog code for adder:
  module fulladder(
    input a,
    input b,
    input c_in,
    output out,
    output c_out
    );
    assign {c_out,out}=a+b+c_in;
  endmodule
Synthesis tools convert behavioural codes to gates which can be implemented on FPGA.
Observing the output of the synthesize tool in Xilinx ISE.

## Slide 4: Hardware Design Languages (Verilog)
Example: Behavioural Verilog code for Counter:
    module counter(
    input clk,
    input reset,
    output reg [20:0] counter);
    always @(posedge clk)
    if (reset)
    counter<=0;
    else
    counter<=counter+1;
    endmodule
Observing the output of the synthesize tool in Xilinx ISE.
Observing Sequential and Combinational structures.

## Slide 5: Hardware Design Languages
There are two popular industry standard hardware description languages:
  VHDL
  Verilog
There exists many specific tools and libraries written in either VHDL or Verilog.
VHDL (Very high speed integrated circuit Hardware Description Language) became IEEE standard 1076 in 1987.
The Verilog language has been used far longer than VHDL and became IEEE Standard 1364-1995 (Verilog-95)
  it was launched by Gateway company in 1983.
  Cadence bought Gateway and opened Verilog to the public domain in 1990.
  Extensions to Verilog-95: IEEE Standard 1364-2001 known as Verilog-2001 (support for 2's complement signed variables and ….).
A New Trend in Hardware Description:
  High-level synthesis(HLS): Accept synthesizable subsets of ANSI C/C++/SystemC/MATLAB. Then the code is analysed to create a register-transfer level (RTL) code such as Verilog and VHDL.
New Trend

## Slide 6: Popularity of Verilog HDL
Verilog HDL
  General-purpose
  Easy to learn, easy to use
  Similar in syntax to C
  Supported by logic synthesis tools and simulators.
  Not all constructs are synthesizable
    Example of non synthesizable Command
        module useless;
        initial begin
        $display(“Hello World!”);
        #10 $finish;
        end
        endmodule
  Compare to printf() in C

## Slide 7: ماژول Module
Verilog Basic Building Block
It can communicate with other parts of the project through ports:
  Input ports
  Output ports
  Bidirectional ports
These ports may be real FPGA I/Os or wires inside the design
A module can be defined without any ports.
Ports can be multiple bits wide.
  Example: input [7:0] a;
Module
1
Module
3
Module
2

## Slide 8: Module:definition
Definition of a module
    module <module_name> (<module_port_list>);
    <ports definition>
    <variables definition>
    ...
    <module functionality>
    ...
    endmodule
A Simple Example:
    module halfadd (c,s,a,b);
      input a,b;
      output s,c;
      xor xor_inst (s,a,b) ;
      and and_inst (c,a,b) ;
    endmodule

## Slide 9: Module Ports Declaration
Interface of the module to the environment
  Internals of the module are not visible to the environment
Items to define
  Port list
  Port type: input, output, inout
  Port details (reg or wire, and bit-width)
Example
  module example(sum, c_out, a,b,c_in);
    output reg [3:0]sum;
    output reg c_out;
    input [3:0] a, b; //wire by default
    input c_in; //wire by default
  ...
  <module internals>
  ...
  endmodule

## Slide 10: ANSI C Style Port Declaration Syntax
An easier way to define the ports:
  In Verilog‐2001 the port list can directly follow the module declaration
  module example(
    output [3:0] sum,
    output c_out,
    input [3:0] a, b, //wire by default
    input c_in); //wire by default
  ...
  <module internals>
  ...
  endmodule
Compare it to the traditional style

## Slide 11: Module Hierarchy and Module Instantiation
Modules can be used within other modules.
Module instantiation: employing a module within another module: sub-module.
  This permits hierarchical design and the re-use of modules.
Example: creating a Full Adder
Main Module
Module 2
Module
4
Module
3
module fulladd(c_out, sum, a, b, c_in); //main module
input a, b, c_in;
output c_out, sum;
wire w1, w2, w3;
halfadd M1 (w1, w2, a, b ); //sub-module
halfadd M2 (w3, sum, w2, c_in ); //sub-module
or M3 (c_out, w3, w1 ); // primitive instantiation
endmodule

## Slide 12: Module Instantiation
Illegal instantiation example:
  Nested module definition not allowed
  Note the difference between module definition and module instantiation
Example
  module top_module(q, clk, reset);
    output [3:0] q;
    input clk, reset;
    module sub_module(q, clock, reset);
    :
    <module T_FF internals>
    :
    endmodule// END OF ILLEGAL MODULE NESTING
  endmodule
ILLEGAL MODULE NESTING

## Slide 13: Lexical Conventions (قواعد نوشتاری)
Verilog HDL is a case-sensitive language.
  All keywords are in lowercase.
Names of variables are similar to C in many ways:
    All keywords are lowercase
    Names can use a…z, A…­Z, 0…­9
    Names don't start with 0­…9
Comments
  Comments can be inserted in the code for readability and documentation.
    One-line comments start with "//".
    Multiple-line comment starts with "/*" and ends with "*/".
Examples
a = b && c; // This is a one-line comment
/* This is a multiple line
comment */
/* This is /* an illegal */ comment */

## Slide 14: Data Values
For our logic design purposes, we’ll consider Verilog to have four different bit values:
  0 - Logical 0 or FALSE
  1 - Logical 1 or TRUE
  x, X - Unknown logic value
  z, Z - High impedance condition
Number Representation
  a=6'b0101001; b=4'd14; c=4'hA;
  Format: <size><base_format><number>
    <size> - decimal specification of number of bits (optional)
    <base format> - ' followed by arithmetic base of number (optional)
      <d> <D> - decimal – (default base)
      <h> <H> - hexadecimal
      <o> <O> - octal
      <b> <B> - binary
    <number> - value given in the specified base

## Slide 15: Number Representation
Underscore characters “_” can is used for reading clarity and is ignored by Verilog.
If first character of sized, binary number is
  0, 1, the value is 0-filled up to size.
  x or z,value is extended using x or z, respectively.
Examples:
  6'b010_111 gives 010111
  8'b0110 gives 00000110
  8'b1110 gives 00001110
  4'bx01 gives xx01
  16'H3AB gives 0000_0011_1010_1011
  5'O36 gives 11110
  16'Hx gives xxxxxxxxxxxxxxxx
  23456 // This is a 32-bit decimal number by default
  'hc3 // This is a 32-bit hexadecimal number
Negative numbers
  Put the sign before the <size>
  Examples:
    -6’d3
    4’d-2// illegal
  Two’s complement is used to store the value (the result of subtracting the number from 2N)

## Slide 16: Levels of Abstraction in Verilog
سطوح مختلف توصیف سخت افزار
  سطح توصیف رفتاری :Behavioral (algorithmic) level
    Describe the algorithm used
    Similar to C programming
  سطح انتقال داده: Dataflow level
    Flow of data in the design
  سطح گیت: Gate level
    Interconnect logic gates
  سطح ترانزیستور: Switch level
    Interconnect transistors (MOS transistors)
For design with FPGA devices, transistor level modeling is not appropriate.
RTL Coding: Register-Transfer Level
  Describing a digital circuit in terms of the flow of digital signals (data) between hardware registers, and the logical operations performed on those signals.

## Slide 17: Gate Level Modeling
Similar to module instantiations
Examples
    wire out1, out2, out3, out4, in1, in2, in3;
    and a1 (out1, in1, in2);
    nand nand1 (out2, in1, in2);
    nand nand2 (out3, in1, in2, in3);
    and (out4, in1, in2);
    // No need to instance name.

## Slide 18: Buffers and Not Gates
Simple Example
  buf b1(OUT1, IN);
  not n1(OUT1, IN);
May have more than two outputs
  buf b1_2out(OUT1, OUT2, IN);

## Slide 19: Bufif/Notif Gates
Applicable when multiple drivers drive the signal.
Examples
    bufif1 b1 (out1, in, ctrl);
    bufif0 b0 (out2, in, ctrl);
    //Instantiation of notif gates
    notif1 n1 (out3, in, ctrl);
    notif0 n0 (out4, in, ctrl);
ctrl |  |  |  |  | 
z | x | 1 | 0 | bufif1 | in
x | x | 0 | z | 0 | 
x | x | 1 | z | 1 | 
x | x | x | z | X | 
x | x | x | z | Z | 
ctrl |  |  |  |  | 
z | x | 1 | 0 | notif1 | in
x | x | 1 | z | 0 | 
x | x | 0 | z | 1 | 
x | x | x | z | X | 
x | x | x | z | Z | 

## Slide 20: Arrays of Gate Instances
Multiple instantiations
  wire [7:0] OUT, IN1, IN2;
  nand n0(OUT[0], IN1[0],IN2[0]);
  nand n1(OUT[1], IN1[1],IN2[1]);
  nand n2(OUT[2], IN1[2],IN2[2]);
  nand n3(OUT[3], IN1[3],IN2[3]);
  nand n4(OUT[4], IN1[4],IN2[4]);
  nand n5(OUT[5], IN1[5],IN2[5]);
  nand n6(OUT[6], IN1[6],IN2[6]);
  nand n7(OUT[7], IN1[7],IN2[7]);
Array of instances
  wire [7:0] OUT, IN1, IN2;
  nand n[7:0](OUT, IN1, IN2);

## Slide 21: Example
module mux4_to_1 (output out, input i0, i1, i2, i3, s1, s0);
  wire s1n, s0n;
  wire y0, y1, y2, y3;
  not (s1n, s1);
  not (s0n, s0);
  and (y0, i0, s1n, s0n);
  and (y1, i1, s1n, s0);
  and (y2, i2, s1, s0n);
  and (y3, i3, s1, s0);
  or (out, y0, y1, y2, y3);
endmodule

## Slide 22: Data Types In Verilog
There are two main data types in Verilog.
  Nets.
    Used for structural connectivity
    Similar to real wires
  Registers.
    Abstraction of storage (May or may not be real physical storage)
Properties of Both
  Informally called signals
  May be either scalar (one bit) or vector (multiple bits)

## Slide 23: Net Data Type
wire
  Most important net type.
  connectivity only; no logical
  Wires are “continuously assigned” values and do not “remember”, or store, information.
  This behaves much like an electrical wire...
  Default Value: z
Example
  Full adder syntax:
    wire w1, w2, w3;
    Add_half M1 ( w1, w2, a, b );
    Add_half M2 ( sum, w3, w1, c_in ); // child module
    or ( c_out, w2, w3 ); // primitive instantiation
  wire gnd_wire = 1’b0;
  Vector of wire: wire [msb_index : lsb_index] data_id;
  Example:
      wire [7:0] bus;
      wire [31:0] busA, busB, busC;
      wire [0:7] flag;

## Slide 24: Register Data Types
Registers are “behaviorally assigned” values and “remember”, or store, information until the next value assignment is made.
The name “reg” does not mean it must be implemented as a physical register! But it could be!
  Default value: x
Examples
  reg a, b, c=0;
  reg reset;
  initial // this construct will be discussed later
  begin
    reset = 1'b1; //initialize reset to 1 to reset the digital circuit.
    #100 reset = 1'b0; // after 100 time units reset is deasserted.
  end
    Vector of register: Exampel reg [7:0] a;
    reg/wire vectors are unsigned numbers, unless specified
  Signed Register Declaration
  reg signed [63:0] m; // 64 bit signed value, 2’s complemenmt

## Slide 25: Other Register Data Types: integer, real
Integer (32 bit register, Default value: 0)
  integer p,m,n;
  Bit width: implementation-dependent (at least 32-bits)
  Designer can also specify a width: integer [7:0] tmp;
  Very similar to a vector of reg
    integer variables are signed numbers
  reg signed [31:0] n=0; // 32 bit signed value
Real (Default value: 0)
  Decimal notation: 12.24 Scientific notation: 3e6(=3*10^6)
  When a real value is assigned to an integer, the real number is rounded off to the nearest integer.
  Example: real delta;
      integer i;
      initial delta=4e10;
      initial delta=2.13;
      initial i = delta; // i gets the value 2

## Slide 26: Register Data Types: Time (will be seen in examples)
Used to store values of simulation time
Keyword: time
Bit width: implementation-dependent (at least 64)
$time system function gives current simulation time
Example:
  time save_sim_time;
  initial
  save_sim_time = $time;

## Slide 27: Variable Vector Part Select
Using a variable part select, one can choose parts
    reg[255:0] data1;
    reg[0:255] data2;
    reg[7:0] byte;
    byte = data1[31-:8]; // => data1[31:24]
    byte = data1[24+:8]; // => data1[31:24]
    byte = data2[31-:8]; // => data2[24:31]
    byte = data2[24+:8]; // => data2[24:31]
The starting bit can also be a variable. The width has to be constant. Therefore, one can use the variable part select in a loop to select all bytes of the vector.
    for (j=0; j<=31; j=j+1)
    byte = data1[(j*8)+:8]; //Sequence is [7:0], [15:8]... [255:248]
    //Can initialize a part of the vector
    data1[(byteNum*8)+:8] = 8'b0; //If byteNum= 1, clear 8 bits [15:8]

## Slide 28: Memories and Multi-dimensional arrays
Allowed for all data types
  Multi-dimensional
Syntax:
<data_type> [msb_index : lsb_index] <var_name> [start_idx : end_idx] .... [start_idx: end_idx];
For multi-dimensional arrays, indexes need to be provided for each dimension.
Examples:
    reg [0:7] R [3:0];
    integer count [0:7];
    reg [10:0] port_id [7:0];
    reg bool[31:0];
    integer matrix[4:0][0:16];
    reg [63:0] array_4d [15:0][7:0][7:0][255:0];
    wire [7:0] w_array2 [5:0];
    initial begin
      array_4d[0][0][0][0][15:0] = 0;
      array_4d[0][4][3][0] = 0;
      port_id= 0; // Illegal
      matrix [1] = 0; // Illegal
      R [1:2] = 0; // Illegal
    end
It is important not to confuse arrays with net or register vectors. A vector is a single element that is n-bits wide. On the other hand, arrays are multiple elements that are 1-bit or n-bits wide.

## Slide 29: Parameters
Constants defined in a module
Keyword: parameter.
        module DUT (s, Out);
          parameter n = 3;
          parameter S0 = 4;
          input [n‐1:0] s;
          output [n:0] Out;
          wire [n:0] Out;
          assign Out = S0;
        endmodule

## Slide 30: Module Ports Declaration rules
All ports are wire by default
  No need to declare it again as wire
If expected to be reg, the port needs to be declared again
  Input ports could not be of type reg.
  output ports could be of type reg.
Example: the q port in DFF module
    module DFF(q, d, clk, reset);
      output q;
      reg q; // Output port q holds value => reg
      input d, clk, reset;
      ...
    endmodule

## Slide 31: Port Mapping rules in Module Instantiation
Connecting by ordered list
  More intuitive for beginners.
  Mostly used when having few ports.
Connecting by name
  Used when having more ports.
  Gives independence from the order of ports.
The order of ports in the port list of a module can be changed without changing the instantiations.
    module Top;
    ...
    fulladd4 fa_ordered(
    SUM, C_OUT,
    A, B, C_IN);
    ...
    endmodule
    module Top;
    ...
    fulladd4 fa_byname(
    .c_out(C_OUT),
    .sum(SUM),
    .b(B),
    .a(A));
    ...
    endmodule

## Slide 32: Port Connection Rules
Width matching
  Legal to connect items of different sizes
  A warning may be issued by Verilog simulator
Unconnected ports
  Allowed in Verilog
  Example: module fulladd(c_out ,sum, a, b, c_in);
    Instants:
    fulladd fa1( ,SUM, A, B, C_IN); // port c_out is unconnected
    fulladd fa2( .sum(SUM), .a(A), .c_in(1’b0), .b(B));

## Slide 33: Examples: 4-bit full adder
  module fulladd4(
  output [3:0] sum,
  output c_out,
  input [3:0] a, b,
  input c_in);
  wire c1, c2, c3;
  // Instantiate four 1-bit full adders.
  fulladd fa0(c1, sum[0], a[0], b[0], c_in);
  fulladd fa1(c2, sum[1], a[1], b[1], c1);
  fulladd fa2(.c_out(c3), .sum(sum[2]),.a(a[2]),.b(b[2]), .c_in(c2));
  fulladd fa3(.c_out(c_out),.sum(sum[3]),.a(a[3]),.b(b[3]), .c_in(c3));
  endmodule

## Slide 34: Hierarchical Names
Hierarchical names
    fulladd4 fulladd4.sum fulladd4.fa4.b
    fulladd4.fa1 fulladd4.fa1.c_in fulladd4.fa1.M1
fulladd4
fa1
fulladd
fa4
fulladd
M2
halfadd
M1
halfadd
......
  sum, c_out,
  a, b, c_in
    a, b, c_in, w1, w2, w3, …
    M1, M2

## Slide 35: Test and Verification
Testbench Module
Stimulus Generation
Checking Outputs of DUT
Design Under Test (DUT)

## Slide 36: Testbench for FullAdder
Testbech
    `timescale 1ns/1ps
    module testbench;
    reg a,b,c_in;
    wire c,s;
    fulladd fulladd_inst(c,s,a,b,c_in);
    initial begin
    a=0;
    b=0;
    c_in=0;
    #5 a=1;
    #5 b=1;
    #5 c_in =1;
    end
    endmodule
    module fulladd ( c_out,sum, a, b, c_in ); input a, b, c_in;
    output c_out, sum;
    wire w1, w2, w3;
    halfadd M1 ( w1, w2, a, b );
    halfadd M2 ( w3, sum, w2, c_in );
    or M3( c_out, w3, w1 );
    endmodule

## Slide 37: Testbench for mux4_to_1
`timescale 1ns/1ps
module stimulus;
  reg IN0, IN1, IN2, IN3;
  reg S1, S0;
  wire OUTPUT;
  mux4_to_1 mymux(OUTPUT, IN0, IN1, IN2, IN3, S1, S0);
  initial begin
    IN0 = 1; IN1 = 0; IN2 = 1; IN3 = 0;
    #10 $display("IN0= %b, IN1= %b, IN2= %b, IN3=%b\n",IN0,IN1,IN2,IN3);
    S1 = 0; S0 = 0;
    #10 $display("S1 = %b, S0 = %b, OUTPUT = %b \n", S1, S0, OUTPUT);
    S1 = 0; S0 = 1;
    #10 $display("S1 = %b, S0 = %b, OUTPUT = %b \n", S1, S0, OUTPUT);
    S1 = 1; S0 = 0;
    #10 $display("S1 = %b, S0 = %b, OUTPUT = %b \n", S1, S0, OUTPUT);
    S1 = 1; S0 = 1;
    #10 $display("S1 = %b, S0 = %b, OUTPUT = %b \n", S1, S0, OUTPUT);
  end
endmodule

## Slide 38: Design process (1)
Library IEEE;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
entity RC5_core is
port(
clock, reset, encr_decr: in std_logic;
data_input: in std_logic_vector(31 downto 0);
data_output: out std_logic_vector(31 downto 0);
out_full: in std_logic;
key_input: in std_logic_vector(31 downto 0);
key_read: out std_logic;
);
end AES_core;
Verilog description
Functional Simulation
Post Synthesis Simulation
Synthesis
Implementation
(Mapping, Placing & Routing)
Timing Place and Route
Simulation

## Slide 39: Simulator Tools
ModelSim
  Mentor Company
ISIM
  Xilinx
Active-HDL
  Aldec Company
.... Many other simulations

## Slide 40: Hierarchical Design
Two Design Methodologies
  Top – Down
    Complete understanding of the system.
    No coding can begin until a sufficient level of detail has been reached
    Placing black boxes stubs instead real modules.
    Increase the delay of testing the ultimate system until significant design is complete.
    Bottom-Up
    Emphasizes coding and early testing,
    as soon as the first module has been specified.
    Increases the risk of design (no clear idea of how the sub-modules link to each other.
    Re-usability of code is one of the main benefits of the bottom-up approach
In practice we use a mixture of them.