## Slide 1: Dataflow Level
  احسان یزدیان
  زمستان 1403
باسمه تعالی

## Slide 2: Levels of Abstraction in Verilog
سطوح مختلف توصیف سخت افزار
  سطح توصیف رفتاری :Behavioral (algorithmic) level
  سطح انتقال داده: Dataflow level
  سطح گیت: Gate level
Continuous assignment
  Realized as connection or wire in the design
  The assign keyword
      module my_and(output out, input in1, in2);
      ....
      assign out = in1 & in2;
      ....
      endmodule

## Slide 3: Continuous assignments انتساب پیوسته
Used for Combinational Logic Implementation
All assign statements operate concurrently.
Syntax: assign LHS = RHS;
  The left hand side, LHS, must be a wire.
  The right hand side, RHS, may be a wire, a reg, a constant, or expressions with operators using one or more wires, regs, and constants.
Two types of continuous assignments:
  Explicit Continuous Assignment
  Implicit Continuous Assignment
Recommendation : Use Explicit Continuous Assignment to make your code more readable
wire x;
assign x=in1|in2;
//the same as:
wire x=in1|in2;

## Slide 4: Gate Level vs. Dataflow Modeling
Gate Level Model
module mux4_to_1 (output out, input i0, i1, i2, i3, s1, s0);
wire s1n, s0n, y0;
Wire y1, y2, y3;
  not not1(s1n,s1);
  not not2(s0n,s0);
  and and1(y0,i0,s1n,s0n);
  and and2(y1,i1,s1n,s0);
  and and3(y2,i2,s1, s0n);
  and and4(y3,i3,s1, s0);
  or or1(out,y0,y1,y2,y3);
endmodule
Dataflow Model
module mux4_to_1 (output out, input i0, i1, i2, i3, s1, s0);
wire y0,y1,y2,y3;
  assign y0 = ~s1 & ~s0 & i0;
  assign y1 = ~s1 & s0 & i1; assign y2 = s1 & ~s0 & i2;
  assign y3 = s1 & s0 & i3;
  assign out = y0|y1|y2|y3;
endmodule
Could be combined in a single statement

## Slide 5: Operators
Operators in Verilog are similar to operators you might find in other programming languages.
Operator category | Operators symbol
Arithmetic | * / + -% **
Logical | ! && ¦¦
Relational | > < <= >=
Equality | == != === !===
Bitwise | ~ & ¦ ^ ^~ ~^
Reduction | & ~& ¦ ~¦ ^ ~^ ^~
Shift | >> << >>> <<<
Concatenation | { }
Replication | { { } }
Conditional | ? :

## Slide 6: Operators
Arithmetic operators:
  + Addition.
  - Subtraction
  * Multiplication
  / Division (Truncates fractional part).
  % Modulus (Remainder from division of two numbers)
  ** Power (raises e to the power f)
Examples:
wire [4:0] a,b,c,d; //evaluates to 1
assign b= -7 % 2; //evaluates to -1, takes sign of first operand
assign c= -7 / 2; //evaluates to -3
assign d= b+c*a;
Be careful of width of the output number.
  Sum: May add one bit
  Multiply: Width of output may be sum of the width of input numbers.
  Examples:
    wire [7:0] a, b;
    wire [8:0] sum;
    assign sum=a+b;
    reg [5:0] a,b;
    wire [11:0] mult;
    assign mult=a*b;

## Slide 7: Operators
relational operators: (output values: 0,1,x)
  > Greater than.
  < Less than.
  >= Greater than or equal.
  <= Less than or equal.
Dyadic comparison operators:
  == Equality operator ( z, x are invalid).
  === Identity operator (z, x are valid).
  != Not equal.
  !== Not identical.
Examples:
a = 2'b10, b = 2'b1x, c = 2'b1z
a == b a === b b == 2’b1x b !== c
(x) (0) (x) (1)

## Slide 8: Operators
Logical operators:
  && Binary logical AND.
  || Binary logical OR.
  Non‐zero operand=logical “1”
  Any X/Z operand Z, result is X
shift operators:
  << Shift left.
  >> Shift right.
  A=6’b001100
Arithmetic Shift: (<<<,>>>)
  arithmetic right shift (>>>)
    Shift right specified number of bits, with value of sign bit if expression is signed, othewise all with zero.
  assign A=$signed(test1) >>> 1 ; // test1 is not a signed number
  assign test3= test2 >>> 1 ; // test2 as signed type
Operation | Result
4’b1010 && 4’b1100 | 1
2’b11 ¦¦ 2’b00 | 1
!(4’b0010) | 0
2’b1X && 2’b11 | x
Operation | Result
B = A >> 1 | B = 6’b000110
C = A << 2 | C = 6’b110000
D = A >> 3 | D = 6’b000001

## Slide 9: Operators
Bit-wise operators:
  & Bit-wise logical AND.
  | Bit-wise logical OR.
  ^ Bit-wise logical XOR.
  ~^ Bit-wise logical XNOR.
  ~ Bit-wise negation
Bitwise vs. Logical operators
Bit-width mismatch issue
Operation | Result
1010 & 1100 | 1000
1010 ¦ 1100 | 1110
~1010 | 0101
1101 ^ 0100 | 1001

## Slide 10: Operators
Concatenation.
  A = 1'b1;
  B = 2'b00;
assign {carry,sum}=a+b+c_in;
wire [7:0] a, shifted_a;
assign shifted_a={a[0],a[7:1]};
Replication.
Operation | Result
{A,B} | 3’b100
{B,A,B} | 5’b00100
{A,3’b001,B} | 6’b100100
Operation | Result
{3{A},B} | 5’b11100
{3{B},2{A}} | 8’b00000011
{{3{A}}, 2’b01,{2{B}}} | 9’b111010000

## Slide 11: Conditional Operator
Conditional Operator
assign D = S ? B:C;
D = B if S=1
D = C if S=0;
A simple Example
reg [7:0] a;
wire [3:0] out;
wire control;
assign out = (control==1’b1) ? a[3:0] : a[7:4];
// the above line can be replaced with the following
//assign out = (control) ? a[3:0] : a[7:4];

## Slide 12: Example : Bus Mux
module 4_input_mux (E, B, C, F, S1, S2 , D);
input [3:0] E,B,C,F;
input S1, S2;
output[3:0] D;
assign D = ({S1,S2}==2’b00)? F:
({S1,S2}==2’b01)? E:
({S1,S2}==2’b10)? C:B;
endmodule

## Slide 13: Example Design In Dataflow Level
Write a module to compute the following equation:
  out
Assume that inputs are 8 bit width.
Calculate The bit width of the output in differenet cases.
  Answer:
    x+y+z : 10 bits
    X*y : 16 bits
    X+5*y ≡ (1+5)*x = 6*x : 11 bits
View the results of simulations for different input data.

## Slide 14: Modeling real hardware delays in Verilog
In real circuits, logic gates have delays associated with them, represent two different physical concepts:
  The RC circuit seen at the node
  propagation delays of electrical elements
Modeling hardware delays are very important in REAL simulations:
  Post-synthesis simulation
  Post-route simulation
Verilog provides the mechanism to associate delays with gates.
  Rise, Fall and Turn-off delays.

## Slide 15: Delay Types
Rise Delay
  output transition to 1 from another value (0, x, z).
Fall Delay
  output transition to 0 from another value (1, x, z).
Turn-Off Delay
  Associated with a gate output transition to z from another value (0, 1, x).

## Slide 16: Delays in Gate-Level Modeling
Delay are shown by # sign in all verilog modeling levels
  Delay of delay_time for all transitions
  and #(delay_time) a1(out, i1, i2);
  Rise and Fall Delay Specification
  Turn-off delay is the minimum of the two
  and #(rise_val, fall_val) a2(out, i1, i2);
  Rise, Fall, and Turn-off Delay Specification
  and #(rise_val, fall_val, turnoff_val) b1 (out, in, control);
  Examples:
  xor #(3) a(out,in1, in2)
  or #(3,4) a(out,in1, in2)
  and #(3, 4, 5) a(out,in1, in2)

## Slide 17: Delays in Dataflow Modeling
Regular Assignment Delay
assign #10 out1 = in1 ^ in2;
assign #(10,8) out2 = in1 & in2;
Net Declaration Delay
  wire #2 out;
  assign #5 out = in1 & in2;
  2 time unit delay on wire out
  5 time units of delay for AND gate
  Any change in in1 or in2 reflects on out after 7 time unit delay

## Slide 18: Example
assign #(5,7,1) out=(a==1);
// Delay in a continuous assign
A pulse of width less than the specified assignment delay is not propagated to the output.
Observing the results on ModelSim and ISIM.

## Slide 19: Min/Typ/Max Delays
Min/Typ/Max Values
  Another level of delay control in Verilog
  Each of rise/fall/turnoff delays can have min/typ/max values
  not #(min:typ:max, min:typ:max, min:typ:max) n(out,in)
Example:
  xor #(1:4:8,4:5:6) xor_inst (out,a,b);
Only one of Min/Typ/Max values can be used in the entire simulation run
  It is specified at start of simulation, and depends to the simulator used
    ModelSim> vsim +mindelays.
    ModelSim> vsim +typdelays.
    ModelSim> vsim +maxdelays.
  Typ delay is the default

## Slide 20: Example Design In Dataflow Level
Write a module to compute the following equation:
  out
View the results of the post place and rout simulation model of computing this equation:
Comparing the results for different rate of input data.
  Argue the unknown values in high frequency values.
Describing the effects of the real delays in the hardware.

## Slide 21: …. Back to FPGA structure
Combinatorial Logic
A
B
C
D
Z
Look-Up Tables
  FPGA uses SRAM memory instead of Combinatorial logic.
    Capacity is limited by the number of inputs, not by the complexity
Benefits:
  Delay through the LUT is constant
  It is simpler to design.
A | B | C | D | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
 | . | . | . | 
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
LUT
A
B
C
D
Z

## Slide 22: Basic Components of FPGA
A typical Slice in 3 Series FPGAs
LUT
Carry
LUT
Carry
D
Q
CE
PRE
CLR
D
Q
CE
PRE
CLR
Simplified Slice Structure
Flip-Flops are used to implement sequential logics.
LUT
LUT
LUT
LUT
0 1
A typical Slice in 7 Series FPGAs
Notes: The major parts of a slice include two Look-Up Tables (LUTs), two sequential elements, and carry logic.
The LUTs are known as the F LUT and the G LUT. The sequential elements can be programmed to be either registers or latches.
The next several slides cover the LUT, the carry logic, and the flip-flops in detail.

## Slide 23: Connecting Look-Up Tables
CIN
Switch
Matrix
COUT
COUT
Slice S0
Slice S1
Local Routing
Slice S2
Slice S3
CIN
SHIFT
A typical CLB
FPGA has Large Number of CLBs (Configurable Logic block) and Interconnections.
Local routing provides feedback between slices in the same CLB, and it provides routing to neighboring CLBs
Notes: Look-Up Tables (LUTs) are also called Function Generators (FGs).

## Slide 24: CLB Inteconnections
Connections between CLBs and other resources use the fabric routing resources
  Routing lines connect to the switch matrixes adjacent to the resources
A switch matrix provides access to general routing resources
The mapping of logical connections to these physical routing resources is entirely managed by the router software.

## Slide 25: FPGA Structure
Basic components
  Configurable Logic (CLBs)
  Contain combinatorial logic and register resources
Programmable Interconnection
Programmable Input/Output circuit
  Interface between the FPGA and the outside world
  Each I/O supports 40+ voltage and protocol standards, including
    LVCMOS, LVDS, LVPECL, SSTL, HSTL, …
  Each pin can be input, output and 3-state.
  Each pin can be individually configured.

## Slide 26: FPGA Structure
Programmable Clock Generator
  Global clock buffers
Macro components
  Multiplier ( large combinational logic)
  Random Access Memory (Large Density)
  Read Only memory (Large Density)
  CPU
  Rocket IO
  DSP blocks

## Slide 27: FPGA Structure (Common Blocks)
I/O Blocks (IOBs)
Configurable
Logic Blocks (CLBs)
Clock Management
Block SelectRAM™
resource
Dedicated multipliers
Programmable interconnect

## Slide 28: Some New Features
1 Gbps SelectIO™ ChipSync™ Source synch, XCITE Active Termination
Smart RAM
New block RAM/FIFO
Xesium Clocking Technology
500 MHz
PowerPC™ 405
with APU Interface 450 MHz, 680 DMIPS
Tri-Mode
Ethernet MAC 10/100/1000 Mbps
RocketIO™ Multi-Gigabit
Transceivers 622 Mbps–10.3 Gbps
XtremeDSP™ Technology Slices 256 18x18 GMACs
Advanced CLBs 200K Logic Cells

## Slide 29: FPGA Vendors
Xilinx, Inc.
    SoC (System on Chips: ARM+FPGA): Zynq
    High Performance
        Virtex: Virtex7, Virtex6, ….
    Low Cost
        Kintex
        Artix
        Spartan: Spartan6, Spartan3, Spartan2, Spartan
Altera Corp.
    Stratix
    Arria
    Cyclone
  Lattice
  Atmel
Flash and Antifuse based:
  Altera (MAX-II)
  Actel Corp.
  Quick Logic Corp.
Share over 89% of the market. (2016)
Incomes are in million$

## Slide 30: Xilinx vs. Altera
Founded | 1983, 34 years ago
Key people | John Daane (CEO) Dan McNamara (Intel PSG leader)
Products | FPGAs, CPLDs, Embedded Processors, ASICs
Revenue | US$ 1.783 billion (2013)
Operating income | US$584.1 million (2013)
Net income | US$556.8 million (2013)
Total assets | US$4.658 billion (2013)
Total equity | US$3.333 billion (2013)
Number of employees | 2,884 (December 2011)
Parent: Intel داده ها قدیمی است چون عملا پس از خریده شدن توسط Intel آمار جداگانه ای از این شرکت نیست. | 
Founded | 1984; 33 years ago
Key people | Dennis Segers Chairman of the Board Moshe N. Gavrielov President CEO Director
Products | FPGAs, CPLDs
Revenue | US$ 3.06 billion (2019) US$ 2.213 billion (2016)
Operating income | US$745.054 million (2018) US$ 669.881 million (2016)
Net income | US$ 622.512 million (2017) US$ 550.867 million (2016)
Total assets | US$ 4.740 billion (2017) US$ 4.819 billion (2016)
Number of employees | 4,014 - (June 2018)

## Slide 31: Example of resources on Virtex-7
Each 7 series FPGA slice contains four LUTs and eight flip-flops;
Two types of slices:
  SLICEM: Full slice
    LUT can be used for logic and memory/SRL
  SLICEL: Logic and arithmetic only (not memory)