## Slide 1: Employing Primitives and Cores In Design
Ehsan Yazdian

## Slide 2: FPGA Dedicated Resources
    Primitives: FPGA components that are native to the FPGA you are targeting
    These Dedicated resources are faster than a LUT/flip-flop implementation and consume less power
    DSP Blocks, FIFO, block RAM, Clock Management DCMs and PLLs, ......

## Slide 3: Using Dedicated Blocks
Offers more performance than soft implementations

## Slide 4: FPGA Resources
Shift register LUT (SRL16E/ SRLC32E)
Carry logic
DCM / PLL
DSP Blocks
Global clock buffers (BUFG)
Memories
Global clock buffers (BUFGCE, BUFGMUX, BUFGDLL)

## Slide 5: Primitive: Digital Clock Manager
Phase Shifting
  provides four phases of the input frequency (CLKIN): shifted 0°, 90°, 180°, and 270°
Frequency Synthesis
  generate any output frequency: multiplying Input freq. by M and simultaneously divided by D, where M can be any integer from 2 to 32 and D can be any integer from 1 to 32.

## Slide 6: Block RAM
Memory Elements
Can be used to implement FIFOs.
Programmable Data Width
  Each port can be configured as 16K × 1, 8K × 2, 4K × 4, 2K × 9 (or 8), 1K × 18 (or 16), or 512 x 36 (or 32).
For example every Spartan-6 FPGA has between 12 and 268 dual-port block RAMs, each storing 18 Kb. Each block RAM has two completely independent ports that share only the stored data.

## Slide 7: Digital Signal Processing Slices
DSP48 blocks in Xilinx FPGA
Consists of a dedicated 18 × 18 bit two's complement multiplier and a 48-bit accumulator.

## Slide 8: Other Resources
Advanced I/O
  50 Different Output Standards
GTX transceivers
  150 Mbps to 6.5 Gbps
  Support many popular high speed standards
  PCI express, OC-48, Gigabit Ethernet
Embedded Processor
  Some FPGAs has embedded CPU Unit.
  Zynq-7000 (SoC): Dual Cortex-A9 ARM Processing System

## Slide 9: Other Resources
PLL
  Jitter filter for incoming clocks in conjunction with the DCMs.
  Voltage-controlled oscillator (VCO) with a frequency range of 400 MHz to 1,080 MHz.
Clock Distribution Resources
  High fanout, short propagation delay, and extremely low skew clock lines
  For example: 16 global-clock lines in Spartan-6 FPGA.
I/O Clocks
Serial Shift registers, Carry logics, EMAC, .....

## Slide 10: Instantiation versus Inference
Instantiate a component when you must dictate exactly which resource is needed
  The synthesis tool is unable to infer the resource
  The synthesis tool fails to infer the resource
Xilinx recommends inference whenever possible
  Inference makes your code more portable
Can be inferred by all synthesis tools
  Shift register LUT (SRL16E/ SRLC32E)
  Carry logic
  Multipliers and counters using the DSP48E
  Global clock buffers (BUFG)
  I/O registers (single data rate)
Can be inferred by some synthesis tools
  Memories
  Global clock buffers (BUFGCE, BUFGMUX, BUFGDLL)
  Some DSP functions
Cannot be inferred by any synthesis tools
  Output DDR registers (Double Data Rate register in I/O blocks)
  DCM / PLL

## Slide 11: Example
Comparing two implementation of ram
  Primitive based (Instantiation)
  Coding based (Inference)

## Slide 12: Using Cores in the Design

## Slide 13: Employing Cores in Your Project
A core is a ready-made function that you can instantiate into your design as a black box
Cores can range in complexity
  Simple arithmetic operators, such as adders, accumulators, and multipliers
  System-level building blocks, such as filters, transforms, and memories
  Specialized functions, such as bus interfaces, controllers, and microprocessors
Some cores can be customized

## Slide 14: Benefits of Using Cores
Save design time
  Cores are created by expert designers who have in-depth knowledge of Xilinx FPGA architecture
Increase design performance
  Cores that contain mapping and placement information have predictable performance that is constant over device size and utilization

## Slide 15: Types of Cores
LogiCORE solutions
  Fully tested, documented, and supported by Xilinx
AllianceCORE solutions
  Sold and supported by Xilinx AllianceCORE solution partners
VHDL and Verilog flow support

## Slide 16: Sample Cores
LogiCORE solutions
  DSP functions
    Time skew buffers, Finite Impulse Response (FIR) filters, transforms, and correlators
  Math functions
    Accumulators, adders, multipliers, integrators, trig functions, and square root
  Memories
    Pipelined delay elements, single- and dual-port RAM
    Synchronous FIFOs
  PCI™ core master and slave interfaces, PCI core bridge
AllianceCORE solutions
  Peripherals
    DMA controllers, programmable interrupt controllers, and UARTs
  Communications and networking
    ATM, Fibre Channel, and Ethernet MAC
    Error Correction
    CTC, 3GPP, Viterbi, and Reed-Solomon
  Video and image processing
  Standard bus interfaces
    PCMCIA, USB, PCI, PCI Express® core

## Slide 17: Sample Code using Cores
Employing DCM to generate different frequancies:
  Input clk: 24 MHz
  Output Clks: 100MHz, 160 MHz
Employing Asynchronous FFIO (First Input, First Output)
Aim: Designing a module to change the rate of data (sample per seconds)
  Input data rate: 100 Msps, output data rate: 160 Msps

## Slide 18
DCM
Async. FIFO
TOP MODULE
Input Clk
24 Mhz
Output Clk
160 Mhz
Output Clk
100 Mhz
Data In
wr_en
full
Data Out
rd_en
empty

## Slide 19: Block Memory Generator Core
Interface Type:
  Native
  AXI4 Interface
Memory Type:
  Single-port RAM
  Simple Dual-port RAM
  True Dual-port RAM
  Single-port ROM
  Dual-port ROM
  Core Document:
    Read Chapter 3, page 54, Operating Mode to learn more about flow of data.
    Chapter 7 for how to create core in ISE.

## Slide 20: CORE Generator Software System
Graphical User Interface of Core Generator
  Data sheets
  Customizable parameters
Generate a core
  Netlist file (NGC), Instantiation template, Behavioral simulation wrapper files (VHD or V).
  Ready for synthesis and implementation and behavioral simulation
  The ISE® software automatically uses wrapper files when cores are present in the design
  Before your first behavioral simulation, you must compile XilinxCoreLib simulation library
  Supports Most of simulation softwares such as ModelSim

## Slide 21: Adding A Core to Design
Compile library for behavioral simulation (one time only)
Core generation and integration
XilinxCoreLib
.NGC
compxlib.exe
Instantiate
Simulate
.VHD, .V
Implement
.VHO, .VEO
Generate Core
.xco