## Slide 1: Behavioural Modeling: Loops Ehsan Yazdian

## Slide 2: Loops
Loops in Verilog
  while, for, repeat, forever
The while loop syntax:
  while (<expression>)
  statement;
The for loop
for(init_expr; cond_expr; change_expr)
statement;
Example:
integer i;
reg [7:0] a [9:0];
reg [7:0] b [9:0];
reg [7:0] out [9:0];
always @(posedge clk) begin
for (i=0;i<10;i=i+1)
begin
out[i]<= a[i] + b [i];
end
end
always @(posedge clkR)
while(cntR != 0)
begin
cntR = cntR-1;
………….
Out = cntR;
end

## Slide 3: Forever Loop
Syntax:
  forever
  statement;
Equivalent to while(1)
//Example 1: Clock generation
//Use forever loop instead of always block
reg clock;
initial
begin
  clock = 1'b0;
  forever #10 clock = ~clock;
end

## Slide 4: The Repeat Loop
Syntax:
  repeat( number_of_iterations )
  statement;
integer count;
initial
  begin
  count = 0;
  repeat(128) begin
    #5 count = count + 1;
  end
end

## Slide 5: Example
Sequence Generation for simulation:
  Transmit the bit sequence 10’b01011_10101 in 10 consecutive positive edges of clock
  Repeat transmission 15 times with 1000 unit of time interval between each transmission (During this interval transmit 1’b1).
reg [9:0] S=10’b01011_10101;
initial begin
repeat (15) begin
repeat (10) begin
out<=S[0];
@(posedge clk) S<={S[0],S[9:1]};
end
out<=1;
#1000;
end
end

## Slide 6: Loops Synthesis
Depending on the usage and synthesis tool, the while, for and repeat loops may be synthesizable.
The loop in an HDL is used to create multiple instances of the hardware
  With a more compact expression
  For the loop to be synthesizable, the synthesizer must be able to completely unroll the loop and resolve the values of all variables it contains- nothing can be dependent on values that are only determined at “run time”, i.e. when the circuit is in operation.
HDL designers will typically use these looping structures to minimize typing a large array of similar assignments that operate on similar elements.
Example: synthesizable for loop
module loop_test(
input clk,
input [4:0] in,
output reg [3:0] out=0
);
integer i;
always @(posedge clk)
for (i=0;i<4;i=i+1)
out[i]<=in[i]&in[i+1];

## Slide 7: Two Types of Block Executions
Sequential Statements
  Statements between begin and end execute sequentially
Parallel Statements
  Statements between fork and join execute in parallel
  If delay or event control is specified, it is relative to the time the block was entered.
  be careful of implicit race conditions.
  fork-join is not synthesizable! (Depends on synthesize tool)
    In RTL coding, non-blocking assignments have the same effect.
initial
fork
  x=1’b0;
  #5 y=1’b1;
  #10 z={x,y};
  #20 w={y,x};
join

## Slide 8: Nested Blocks
Sequential and parallel blocks can be mixed
initial
begin
  #10 x=1’b0;
  fork
    #5 y=1’b1;
    #10 z={x,y};
  join
  #20 w={y,x};
end

## Slide 9: Named blocks
Syntax:
  begin: <name>
  ……
  end
Advantages:
  Can have local variables (local variables are static)
    Their local variables can be accessed using hierarchical names
  Part of the design hierarchy.
Can be disabled
  Keyword: disable
  Disabling a named block terminates all blocks within.

## Slide 10: Example of Disable
//Illustration: Find the first bit with a value 1 in flag
reg [15:0] flag;
reg [7:0] i; //integer to keep count
initial
begin
  flag = 16'b 0010_0000_0000_0000;
  i = 0;
  begin: block1 //The main block inside while is named block1
    reg local_temp;
    while(i < 16)
    begin
      if (flag[i])
      begin
        $display("Encountered a TRUE bit at element number %d", i);
        disable block1; //disable block1 because you found true bit.
      end
      i = i + 1;
    end
  end
end

## Slide 11: System Tasks
The $ sign denotes Verilog system tasks, there are a large number of these
Most useful system tasks:
  $display(“The value of a is %b”, a);
    Used in procedural blocks for text output.
    The %b is the value format (binary, in this case…)
  $monitor(“The value of a is %d”, a);
    displays any changes in the variables.
  $finish;
    Used to finish the simulation.
    Use when your stimulus and response testing is done.
  $stop;
    Similar to $finish, but doesn’t exit simulation.

## Slide 12: Parameters
Constants defined in a module
Keyword: parameter.
Can be overridden individually at compile time. This allows the module instances to be customized.
parameter port_id = 5; // Defines a constant port_id
parameter cache_line_width = 256;
Parameters values can be changed at module instantiation or by using the defparam statement
  This allows the module instances to be customized.
Module behaviour can be altered simply by changing the value of a parameter.

## Slide 13: Overriding Parameter Values
Two ways
  defparam statement
  Module instance parameter value assignment
defparam Statement
module hello_world;
  parameter id_num = 0;
  initial
  $display("Displaying hello_world id number = %d", id_num);
endmodule
module top;
  defparam w1.id_num = 1, w2.id_num = 2;
  hello_world w1();
  hello_world w2();
endmodule

## Slide 14: Module_Instance Parameter Values
Parameter values can be overridden when a module is instantiated.
module top;
//Parameter value assignment by ordered list
hello_world #(1) w1; //pass value 1 to module w1
//Parameter value assignment by name
hello_world #(.id_num(2)) w2;
endmodule

## Slide 15: Overridding multiple parameters
//define module with delays
module bus_master;
parameter delay1 = 2, delay2 = 3, delay3 = 7;
...
endmodule
//Instantiate the modules with new delay values
//Parameter value assignment by ordered list
bus_master #(4, 5, 6) b1(); //b1: delay1 = 4, delay2 = 5, delay3 = 6
bus_master #(9, 4) b2(); //b2: delay1 = 9, delay2 = 4, delay3 = 7(default)
//Parameter value assignment by name
bus_master #(.delay2(4), .delay3(7)) b3(); //b2: delay2 = 4, delay3 = 7
//delay1=2 (default)
endmodule
It is recommended to use the parameter value assignment by name

## Slide 16: local parameters
identical to parameters except that they cannot be directly modified with the defparam statement or by the ordered or named parameter value assignment.
Parameters which their values should not be changed.
localparam state1 = 4'b0001,
state2 = 4'b0010,
state3 = 4'b0100,
state4 = 4'b1000;