## Slide 1: Design Optimization Ehsan Yazdian

## Slide 2: Introduction
Tool optimizations are often not good enough to meet most design constraints if an arbitrary coding style is used.
Three primary physical characteristics which should be optimized:
  Speed
  Area
  Power
Implementation Tradeoffs
Definitions of speed (depending on the context of the problem)
  Throughput
  Latency
  Timing

## Slide 3: Defining the metrics
Throughput: Amount of data that is processed in one clock cycle
  Metric: bits per second
  Goal: High-throughput architectures
Latency: The time between data input and processed data output
  Metric: time or clock cycles
  Goal: Low-latency architectures
Timing: The logic delays between sequential elements
  Metric: clock period and frequency
  Goal: Reduce the combinatorial delay of the critical path
  Has been discussed in previous sessions as combinatorial delay, clk-to-out delay, routing delay, setup timing, clock skew and ….

## Slide 4: High Throughput Design
Concerning the steady-state data rate not latency.
Ford idea: Assembly line
  In the world of digital design we refer to this term as: pipeline
The beauty of a pipelined design is that new data can begin processing before the prior data has finished, much like cars are processed on an assembly line
Pipelines are used in nearly all very-high-performance devices
  CPU instruction sets
  network protocol stacks
  encryption engines
  …..

## Slide 5: Pipelining
Consider a circuit that does N operations per clock cycle at a frequency F. This design performs N*F ops/second.
Pipelining is a technique to trade latency and area to improve throughput by increasing F.
What sets the maximum frequency?
  The maximum delay between flip flops!

## Slide 6: How Pipelining Improves the Throughput?
What causes delay between flip flops?
  Combinational logic to implement the algorithm.
  Wires for distributing signals.
  Timing characteristics of the flip flops themselves. (Setup time, ...)
Partitioning the design into two pieces, with each piece contributing 1/2 of the total delay
Inserting FF’s in middle

## Slide 7: Pipelining
Results…
  Frequency increases; the critical paths are halved.
  Latency in cycles increases; not obvious yet but the latency in real (elapsed time) also increases.
  Area increases; more flip flops required.
What if you partitioned into M equal stages?
  Ideally, your new throughput is N*F*M ops/sec, but …

## Slide 8: Pipeline Example
Individual functions are marked with their delay and cannot be further divided.
Where is the best points to insert pipelining flip flops?

## Slide 9: Cont.
Some signal paths need two flip flops to keep information flow synchronized.
  Old Latency = 19 ns
  Old Throughput = 1 op / 19 ns
  New Latency = 27 ns (3 cycles)
  New Throughput = 1 op / 9 ns

## Slide 10: A Real Example: FIR Filter
module fir(input clk, input validsample,
output [17:0] Y, input [7:0] A, B, C, X);
reg [7:0] X1, X2, Y;
always @(posedge clk)
if(validsample) begin
X1 <= X;
X2 <= X1;
Y <= A* X+B* X1+C* X2;
end
endmodule

## Slide 11: Pipelining The Filter
The critical path of one multiplier and one adder is greater than the minimum clock period requirement for registring.
Pipelining: Adder was separated from the multipliers with a pipeline stage
always @ (posedge clk) begin
if(validsample) begin
X1 <= X; X2 <= X1;
prod1 <= A * X; prod2 <= B * X1;
prod3 <= C * X2;
validsample_reg<=validsample;
end else if (validsample_reg)
Y <= prod1 + prod2 + prod3;
end

## Slide 12: Problems and Conclusion
Computation depends on the result of a previous computation still in the pipeline. We should be careful of placing FF on all of edges in the cut-set.
Conclusion:
  Pipelining is a tool you can use to trade area and latency for throughput.
  In complex designs, you need to be careful of the above problems.

## Slide 13: Pipelining Issues
As M →∞, so does your circuit area and latency.
  Even if that were not true, you will reach a point where you can no longer sub-divide the design.
The flip flop clock-to-out and setup time requirements do not change and set a limit on F, as M →∞.
Your algorithm may not easily partition into M equal stages
  in which case, the increase in F is set by the partition with the longest delay.
Strategy: Focus your attention on placing the pipelining flip flops to isolate the slowest piece of the design and then maintain balance.

## Slide 14: Retiming (Register Balancing)
Improving throughput by decreasing the worst-case delay → increasing F.
Redistribute logic evenly between registers to minimize the worst-case delay between any two registers.
This technique should be used whenever logic is highly imbalanced between the critical path and other paths.

## Slide 15: Simple Example
Solid bars represent flip flops. Assume the design flip flops.
This is an unbalanced, pipelined design.
Retime the circuit without moving the input or output flip flops.

## Slide 16: Solution
Old Latency = 32 ns (2 cycles)
Old Throughput = 1 op / 16 ns
New Latency = 22 ns (2 cycles)
New Throughput = 1 op / 11 ns

## Slide 17: A Real Example
The logic between stages 1 and 2 is the adder for all inputs
There is no logic between the input and the first register (assume the outputs feeding this module are registered)
input [7:0] A, B, C;
reg [7:0] rA, rB, rC;
always @(posedge clk) begin
rA <= A;
rB <= B;
rC <= C;
Sum <= rA + rB + rC;
end
endmodule

## Slide 18: Register Balancing
We can push one of the add operations backward.
always @(posedge clk) begin
rABSum <= A + B;
rC <= C;
Sum <= rABSum + rC;
end

## Slide 19: Retiming Conclusion
Retiming in many cases is not a magic tool and may gain you very little. However in some cases if the initial design is not well enough, retiming may results in substantial improvement.
The decision to use this tool to optimize your design should be based on the critical path of the design and your design constraints.
Nowadays retiming can be done in synthesis tools. However you should take care of significant design structure changes.

## Slide 20: Duplicating Flip-Flops
High-fanout nets can be slow and hard to route
Duplicating flip-flops can fix both problems
  Reduced fanout shortens net delays
  Each flip-flop can fanout to a different physical region of the chip to help with routing
Design tradeoffs
  Gain routability and performance
  Design area increases

## Slide 21: Duplicating Flip-Flops
Explicitly create duplicate flip-flops in your HDL code
  Most synthesis tools have automatic fanout-control features
    However, they do not always pick the best division of loads
Many synthesis tools will optimize-out duplicated flip-flops
  Tel your synthesis tool to keep redundant logicl
    (EQUIVALENT_REGISTER_REMOVAL option in XST).
We can apply attributes on specific registers or levels of hierarchy to specify which registers can or cannot be replicated.

## Slide 22: Implementation Example
PERIOD = 5 ns timing constraint
Implemented with default options
  Longest path = 6.806 ns
  Fails to meet timing constraint
Longest path = 4.666 ns
  Meets timing constraint

## Slide 23: Simple Verilog Example
Many times an additional synthesis constraint needs to be added to ensure that a manually duplicated register is not optimized away by the synthesis tool.
In this example, the XST syntax was used
(*EQUIVALENT_REGISTER_REMOVAL="NO"*) reg ce1,ce2;
// Clock enable register with 64 fanout
// Duplicating once
always @(posedge clk) begin
ce1 <= ce;
ce2 <= ce;
end
always @(posedge clk) begin
if (ce1)
res[31:0] <= a_data[31:0];
end
always @(posedge clk) begin
if (ce2)
res[63:32] <= a_data[63:32];
end

## Slide 24: Resource Sharing
Resource sharing is a technique to trade frequency and latency for area.
Resource sharing is when a single hardware resource (typically area-expensive) is used to implement several operations in the design.
What kind of operations can share hardware?
  Addition, Subtraction, Comparisons.
  Multiplication, Division.

## Slide 25: Resource Sharing Example
Assume a 16x16 multiplier uses 100 area units.
Assume a 4:1 multiplexer uses 1 area unit.
Consider the following block of code:
wire [15:0] a, b, c, d, e, f, g, h, i, j;
reg [31:0] output1, output2;
wire [1:0] op;
always @* begin
output1 = a * b;
case (op)
2’b00: output2 = c * d;
2’b01: output2 = e * f;
2’b10: output2 = g * h;
2’b11: output2 = i * j;
endcase
end

## Slide 26: Resource Sharing
A simple implementation uses:
  A multiplier to generate output1.
  Four multipliers, followed by a 32-bit wide 4:1 multiplexer to generate output2.
  Area cost is 532 area units.
A better implementation uses:
  A multiplier to generate output 1.
  Two 16-bit wide 4:1 multiplexers followed by a multiplier to generate output2.
  Area cost is 200 + 2*16=232 area units.

## Slide 27: Some Other Ideas for Timing and Area Optimization (Less Important)

## Slide 28: Other Timing Optimizations Techniques
Parallel structures
  Separating sequentially executed operations into parallel operations.
  For example, we can break the multipliers into independent operations.
  X = {A, B}
    A is the 4 most significant bits
    B is the 4 least significant bits
  For instance : X2 can be calculated as follows
X * X = {A, B} * {A, B} = {A *A , B*B} + 2*(A *B)<<4;
= {A *A , B*B} + (A *B)<<5;

## Slide 29: Reordering paths
Diverting operations in a critical path to a noncritical path.
Example:
module randomlogic( output reg [7:0] Out, input [7:0] A, B, C,
input clk, input Cond1, Cond2);
always @(posedge clk)
if(Cond1)
Out <= A;
else if(Cond2 && (C < 8))
Out <= B;
else
Out <= C;
endmodule

## Slide 30: Reordering paths
Moving one of the gates out of the critical path in series with the comparator.
wire CondB = (Cond2 & !Cond1);
always @(posedge clk)
if(CondB && (C < 8))
Out <= B;
else if(Cond1)
Out <= A;
else
Out <= C;

## Slide 31: IMPACT OF RESET ON AREA
There are a number of considerations to take into account relative to area when designing a reset structure.
An improper reset strategy can create an unnecessarily large design and inhibit certain area optimizations.
  Resources Without Reset
  Resources Without Set
  Resources Without Asynchronous Reset
  Resetting RAM
  Utilizing Set/Reset Flip-Flop Pins

## Slide 32: Resources Without Reset
Insistence on defining a global set/reset condition for every flip-flop.
  Although this may seem like good design practice, it can often lead to a larger design
The reason for this is
  Certain functions can be optimized according to the fine-grain architecture of the FPGA without reset input.
  Bringing a reset into every synchronous element can cause the synthesis and mapping tools to push the logic into a coarser implementation

## Slide 33: Resources Without Reset
There exists built-in shift-register resources in the FPGA: SRL16
  No resets are defined for the SRL16 resources.
Example of a simple shift register:
  IMPLEMENTATION 1 : Synchronous Reset
      always @(posedge iClk)
      if(!iReset) sr <= 0;
      else sr <= {sr[14:0], iDat};
  IMPLEMENTATION 2 : No Reset
      always @(posedge iClk)
      sr <= {sr[14:0], iDat};

## Slide 34
Implementation 2
Implementation 1

## Slide 35: Resources Without Reset
The key here is that
  if we wish to take advantage of built-in shift-register resources available in the FPGA, we will need to code it such that there is a direct mapping.
If resets are defined in our design, then the SRL16 unit could not be used as there are no reset control signals to the resource
Then, shift register would be implemented as discrete flipflops as shown in the next slide

## Slide 36: Resources Without Set
Similar to the previous problem, some internal resources lack any type of set capability.
The multiplier resources in most FPGAs have built-in reset resources while they do not typically have set resources.
An example is that of an 8*8 multiplier
  module mult8(
  output reg [15:0] oDat,
  input iReset, iClk,
  input [7:0] iDat1, iDat2);
  always @(posedge iClk)
  if(!iReset) oDat <= 16’hffff;
  else oDat <= iDat1 * iDat2;
  endmodule

## Slide 37: Resources Without Set
If the set functionality as described above (16’hffff instead of simply 0) is required, the used area would be much larger.
In the set scenario, an additional gate for each output is required to set the output when the reset is active.
The reset on the multiplier, in this case, will go unused.
Affects both timing and area usage.

## Slide 38: Resources Without Async. Reset
Built-in DSP resources are used to multiply–accumulate functions.
The DSP structures inside a many Xilinx FPGA, for example Virtex-4 devices, have only synchronous reset capabilities.
always @(posedge iClk or negedge iReset)
if(!iReset) begin
multfactor <= 0;
oDat <= 0;
end
else begin
multfactor <= (iDat1 * iDat2);
oDat <= multfactor + oDat;
end

## Slide 39: Resources Without Async. Reset
To implement an asynchronous reset, the synthesis tool must create additional logic outside of the DSP core.
Built-in RAM resources are similar to the DSP resources and often only synchronous resets are available.
Generally resetting RAM is usually poor design practice, particularly if the reset is asynchronous.

## Slide 40: Utilizing Set/Reset Flip-Flop Pins
Given a particular logic function, the synthesis tool can often use the set and reset pins to implement aspects of the logic and reduce the burden on the look-up tables.
In this case, the synthesis tool may choose to implement the logic using the set pin on a flip-flop.

## Slide 41
Likewise, consider a logic function of the form illustrated in this figure. The AND gate can be eliminated by running the input signal to the reset pin of the flip-flop.

## Slide 42
Reset strategy may prevent synthesis tools from performing this class of optimizations.
Example:
  module setreset( output reg oDat, input iReset, iClk, input iDat1, iDat2);
  always @(posedge iClk or negedge iReset)
  if(!iReset)
  oDat <= 0;
  else
  oDat <= iDat1 | iDat2;
  endmodule

## Slide 43
If we remove the reset pin the same logic can be optimized.

## Slide 44
Moreover we can use both synchronous set and reset signals.
Assume we want to calculate:
  oDat<=!iDat3 & (iDat1 | iDat2);
We can code like this to optimize the area:
  always @(posedge iClk)
  if(iDat3)
  oDat <= 0;
  else if(iDat1)
  oDat <= 1;
  else
  oDat <= iDat2;

## Slide 45
It is not recommended to optimize in this way unless when area is the key consideration

## Slide 46: Simple Example On Pipelining: unrolling the loop
Calculating the 3rd power of X : X^3
Assume 8 bit input.
Software Implementation
  XPower = 1;
  for (i=0;i < 3; i++)
  XPower = X * XPower;
    There is no use for parallelism because a microprocessor only executes one instruction at a time (single core processor)

## Slide 47: iterative implementation
input [7:0] X; input start; reg [7:0] XPower;
always@(posedge clk)
if(start) begin
XPower <= X;
ncount <= 2;
end else if (ncount !== 0) begin
ncount <= ncount - 1;
XPower <= XPower * X;
end

## Slide 48: iterative implementation
Throughput: 8/3, or 2.7 bits/clock
Latency: 3 clocks
Timing: One multiplier delay in the critical path
With this type of iterative implementation, no new computations can begin until the previous computation has completed
This iterative scheme is very similar to a software implementation
Certain handshaking signals are required to indicate the beginning and completion of a computation

## Slide 49: Low Latency Solution
Low Latency Solution:
  always @* begin
  XPower1 = X;
  XPower2 = XPower1*X;
  end
  always @(posedge clk) begin
  XPower = XPower2 * X;
  end
Throughput: 8 bits/clock (assuming one new input per clock)
Latency: Two multiplier delays, 1 clock
Timing: Two multiplier delays in the critical path

## Slide 50: Pipelined Implementation
always @(posedge clk) begin
// Pipeline stage 1
XPower1 <= X;
X_reg2 <= XPower1;
// Pipeline stage 2
XPower2 <= XPower1 * XPower1;
// Pipeline stage 3
XPower <= XPower2 * X_reg2;
end
Throughput: 8/1, or 8 bits/clock
Latency: 3 clocks
Timing: One multiplier delay in the critical path

## Slide 51: Comparison
Comparing pipeline with iterative implementation:
  Both of them have 3 clocks latency
  Both of them have the similar critical path, contained only one multiplier.
  Pipelined implementation improves throughput by a factor 3.
  Pipeline implementation needs more area in this example

## Slide 52: Comparison
Comparing pipeline with low latency implementation:
  Both of them needs same area unless the registers.
  Latency can be reduced by removing pipeline registers, the penalty is clearly in the timing
  Pipeline implementations could theoretically run the system clock period close to the delay of a single multiplier
  In the Low-latency implementation, the clock period must be at least two multiplier delays (depending on the implementation) plus any external logic in the critical path.