## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 9 Multimedia Networking

## Slide 2: Multimedia networking: outline
9.1 multimedia networking applications
9.2 streaming stored video
9.3 voice-over-IP
9.4 protocols for real-time conversational applications: RTP, SIP
9.5 network support for multimedia

## Slide 3: Real-Time Protocol (RTP)
RTP specifies packet structure for packets carrying audio, video data
RFC 3550
RTP packet provides
  payload type identification
  packet sequence numbering
  time stamping
RTP runs in end systems
RTP packets encapsulated in UDP segments
interoperability: if two VoIP applications run RTP, they may be able to work together

## Slide 4: RTP runs on top of UDP
RTP libraries provide transport-layer interface
that extends UDP:
  port numbers, IP addresses
  payload type identification
  packet sequence numbering
  time-stamping

## Slide 5: RTP header
payload type (7 bits): indicates type of encoding currently being used. If sender changes encoding during call, sender
informs receiver via payload type field
  Payload type 0: PCM mu-law, 64 kbps
  Payload type 3: GSM, 13 kbps
  Payload type 7: LPC, 2.4 kbps
  Payload type 26: Motion JPEG
  Payload type 31: H.261
  Payload type 33: MPEG2 video
sequence # (16 bits): increment by one for each RTP packet sent
  detect packet loss, restore packet sequence
payload type
sequence number type
time stamp
Synchronization
Source ID
Miscellaneous fields

## Slide 6: RTP header
timestamp field (32 bits long): sampling instant of first byte in this RTP data packet
  for audio, timestamp clock increments by one for each sampling period (e.g., each 125 usecs for 8 KHz sampling clock)
  if application generates chunks of 160 encoded samples, timestamp increases by 160 for each RTP packet when source is active. Timestamp clock continues to increase at constant rate when source is inactive.
SSRC field (32 bits long): identifies source of RTP stream. Each stream in RTP session has distinct SSRC
payload type
sequence number type
time stamp
Synchronization
Source ID
Miscellaneous fields

## Slide 7: Real-Time Control Protocol (RTCP)
works in conjunction with RTP
each participant in RTP session periodically sends RTCP control packets to all other participants
each RTCP packet contains sender and/or receiver reports
  report statistics useful to application: # packets sent, # packets lost, interarrival jitter
feedback used to control performance
  sender may modify its transmissions based on feedback

## Slide 8: Real Time Streaming Protocol (RTSP)
RFC 2326
Remote media playback control:
  VCR-like user control of display: play, rewind, fast forward, pause, resume, etc…
Similar to HTTP but RTSP servers maintain state
TCP or UDP can be used for the control channel

## Slide 9: RTSP Requests (methods)
Major methods
  􀂾SETUP: allocate resources for a stream and start an RTSP session
  􀂾PLAY: start data transmission on a stream
  􀂾PAUSE: temporarily halt a stream
  􀂾TEARDOWN: free resources and end the stream
Additional methods
  􀂾OPTIONS: get available methods
  􀂾DESCRIBE: get low level description of media object
  􀂾RECORD: start recording a stream
  􀂾REDIRECT: redirect client to new server

## Slide 10: SIP: Session Initiation Protocol [RFC 3261]
long-term vision:
all telephone calls, video conference calls take place over Internet
people identified by names or e-mail addresses, rather than by phone numbers
can reach callee (if callee so desires), no matter where callee roams, no matter what IP device callee is currently using

## Slide 11: SIP services
SIP provides mechanisms for call setup:
  for caller to let callee know she wants to establish a call
  so caller, callee can agree on media type, encoding
  to end call
determine current IP address of callee:
  maps mnemonic identifier to current IP address
call management:
  add new media streams during call
  change encoding during call
  invite others
  transfer, hold calls

## Slide 12: Example: setting up call to known IP address
Alice’s SIP invite message indicates her port number, IP address, encoding she prefers to receive (PCM mlaw)
Bob’s 200 OK message indicates his port number, IP address, preferred encoding (GSM)
SIP messages can be sent over TCP or UDP; here sent over RTP/UDP
default SIP port number is 5060

## Slide 13: Example of SIP message
INVITE sip:bob@domain.com SIP/2.0
Via: SIP/2.0/UDP 167.180.112.24
From: sip:alice@hereway.com
To: sip:bob@domain.com
Call-ID: a2e3a@pigeon.hereway.com
Content-Type: application/sdp
Content-Length: 885
c=IN IP4 167.180.112.24
m=audio 38060 RTP/AVP 0
Notes:
HTTP message syntax
sdp = session description protocol
Call-ID is unique for every call
Here we don’t know Bob’s IP address
  intermediate SIP servers needed
Alice sends, receives SIP messages using SIP default port 506
Alice specifies in header that SIP client sends, receives SIP messages over UDP

## Slide 14: Name translation, user location
caller wants to call callee, but only has callee’s name or e-mail address.
need to get IP address of callee’s current host:
  user moves around
  DHCP protocol
  user has different IP devices (PC, smartphone, car device)
result can be based on:
  time of day (work, home)
  caller (don’t want boss to call you at home)
  status of callee (calls sent to voicemail when callee is already talking to someone)

## Slide 15: SIP registrar
REGISTER sip:domain.com SIP/2.0
Via: SIP/2.0/UDP 193.64.210.89
From: sip:bob@domain.com
To: sip:bob@domain.com
Expires: 3600
one function of SIP server: registrar
when Bob starts SIP client, client sends SIP REGISTER message to Bob’s registrar server
register message:

## Slide 16: SIP proxy
another function of SIP server: proxy
Alice sends invite message to her proxy server
  contains address sip:bob@domain.com
  proxy responsible for routing SIP messages to callee, possibly through multiple proxies
Bob sends response back through same set of SIP proxies
proxy returns Bob’s SIP response message to Alice
  contains Bob’s IP address
SIP proxy analogous to local DNS server plus TCP setup

## Slide 17: SIP example: jim@umass.edu calls keith@poly.edu
1
1. Jim sends INVITE message to UMass SIP proxy.
2. UMass proxy forwards request
to Poly registrar server
2
3. Poly server returns redirect response, indicating that it should try keith@eurecom.fr
3
5. eurecom registrar forwards INVITE to 197.87.54.21, which is running keith’s SIP client
5
4
4. Umass proxy forwards request
to Eurecom registrar server
8
6
7
6-8. SIP response returned to Jim
9
9. Data flows between clients
UMass SIP proxy
Poly SIP
registrar
Eurecom SIP
registrar
197.87.54.21
128.119.40.186