## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 4 Network Layer:
Data Plane
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on middleboxes (and Internet arch), Net neutrality, buffering …
lighter header font

## Slide 2: Network layer: data plane, control plane
Data plane:
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
1
2
3
0111
values in arriving
packet header
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers

## Slide 3: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 4: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 5: Generalized forwarding: match plus action
1
2
0111
3
values in arriving
packet header
Review: each router contains a forwarding table
“match plus action” abstraction: match bits in arriving packet, take action
  generalized forwarding:
    many header fields can determine action
    many action possible: drop/copy/modify/log packet
forwarding table
(aka: flow table)
(aka: flow table)
  destination-based forwarding: forward based on dest. IP address

## Slide 6: Flow table abstraction
flow: defined by header field values (in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Router’s flow table defines router’s match+action rules
Flow table
match
action

## Slide 7: Flow table abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)

## Slide 8: OpenFlow: flow table entries
Match
Action
Stats
Forward packet to port(s)
Drop packet
Modify fields in header(s)
Encapsulate and forward to controller
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer

## Slide 9: OpenFlow: examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
Block (do not forward) all datagrams destined to TCP port 22 (ssh port #)
Block (do not forward) all datagrams sent by host 128.119.1.1
Destination-based forwarding:
*
*
*
*
*
*
51.6.0.8
*
*
*
port6
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
*
*
Firewall:
drop
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
drop
*
128.119.1.1

## Slide 10: OpenFlow: examples
Layer 2 destination-based forwarding:
layer 2 frames with destination MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
*
*
*
*
*
*
*
*
*
port3
22:A7:23:
11:E1:02
*
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS

## Slide 11: OpenFlow abstraction
match+action: abstraction unifies different kinds of devices
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port

## Slide 12: OpenFlow example
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 13: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 14: Generalized forwarding: summary
“match plus action” abstraction: match bits in arriving packet header(s) in any layers, take action
  matching over many fields (link-, network-, transport-layer)
  local actions: drop, forward, modify, or send matched packet to controller
  “program” network-wide behaviors
simple form of “network programmability”
  programmable, per-packet “processing”
  historical roots: active networking
  today: more generalized programming:
  P4 (see p4.org).

## Slide 15: Generalized forwarding: summary
Question: how are forwarding tables (destination-based forwarding) or flow tables (generalized forwarding) computed?
Answer: by the control plane